## Slide 1: Guide to Subnetting

## Slide 2: What is subnetting
Subnetting is the foundation underlying the expansion of both Local Networks & the Internet in today’s world.
Subnetting has become essential knowledge for the Administrator of any network.

## Slide 3: Subnetting, subnets, subnet masks?
Subnetting, a subnet & a subnet mask are all different.
In fact, the Subnetting creates Subnets & is identified by the Subnet Masks.
Subnetting is the process of dividing a network and its IP addresses into segments, each of which is called a subnetwork or subnet.
Subnet = Network = Broadcast Domain = VLAN

## Slide 4: Subnet masks
The subnet mask is the 32-bit number that the router uses to cover up the network address to show which bits are being used to identify the subnet.
In other words, subnet masks help you identify the network ID portion and the host portion of an IP address.
E.g. IP Address 192.168. 1 . 1
Subnetmask 255.255.255. 0
network ID host

## Slide 5: Borrowing Bits to Grow a SubneT
Problem: Given an original network of 192.168.1.0 /24 We need 6 subnetworks.
Step 1:
Convert the required number into binary to get the bit value of that number.
6 Into binary 128 64 32 16 8 4 2 1
Gives us 1 1 0 0 0 0 0 0 1 1 0
Which is 3 bits counting the positions, gives us = 3 bits

## Slide 6: Borrowing Bits to Grow a SubneT
Step 2:
Convert the original subnet mask into binary. /24 or 255.255.255.0 (based on default classful IP subnet masks)
OM 11111111.11111111.1111111.00000000 (/24)
Step 3:
Get the number of borrowed bits and insert that into the OM to get the New Mask (NM)
3bits into NM 11111111.11111111.1111111.11100000 (/27)
3bits

## Slide 7: Borrowing Bits to Grow a SubneT
Step 4:
Note the position of the last bit in relation to your binary conversion chart and make that a significant number.
NM 11111111.11111111.1111111.11100000
128 64 32 16 8 4 2 1
The significant 32 number will help us determine how to increment the subnets.

## Slide 8: Borrowing Bits to Grow a SubneT
Step 5: Now we determine the subnets. We are required 6 subnets, so will increment by 32 until we get 6 subnets
Original IP 192.168.1.0 /24
Note: Since it is a /24, we apply the increments on the last octet.
Simply because /24 is 255.255.255.0 We always increment where the octet has less than a 255 value.
Subnet 1 192.168.1.0
Subnet 2 192.168.1.32
Subnet 3 192.168.1.64
Subnet 4 192.168.1.96
Subnet 5 192.168.1.128
Subnet 6 192.168.1.160

## Slide 9: Borrowing Bits to Grow a SubneT
Step 5: Now we have the 6 subnets, we can now determine IP address ranges. IP Ranges
Subnet 1 192.168.1.0 192.168.1.31
Subnet 2 192.168.1.32 192.168.1.63
Subnet 3 192.168.1.64 192.168.1.95
Subnet 4 192.168.1.96 192.168.1.127
Subnet 5 192.168.1.128 192.168.1.159
Subnet 6 192.168.1.160 192.168.1.191
Subnet 7 192.168.1.192
Do you see the pattern? The far end of the IP range is where the other one begins.

## Slide 10: Borrowing Bits to Grow a SubneT
Step 5: Now we have the IP Ranges, we must determine the valid IP addresses within the ranges. Excluding the Network ID and Broadcast Address for each subnet. IP Ranges
Subnet 1 192.168.1.0 192.168.1.31
Subnet 2 192.168.1.32 192.168.1.63
Subnet 3 192.168.1.64 192.168.1.95
Subnet 4 192.168.1.96 192.168.1.127
Subnet 5 192.168.1.128 192.168.1.159
Subnet 6 192.168.1.160 192.168.1.191
Subnet 7 192.168.1.192
We cant use the first IPs because these are Network ID.
We cant use the last IPs because these are Broadcast IP
So we use the ones in the middle For Subnet1, the valid IPs are .1 to .30